## Slide 2
QUATRA 1000/2000 local software update
Version 07

## Slide 3: QUATRA 1000/2000 need for local update
After 28th October 2023, QUATRA 1000/2000 Network Units require these software images, in order to communicate with the Wave Cloud:
  NU software: 700N036-xxx-057 (where xxx is a region-dependent 3-digit number)
  NU PIC: 700N046-003-048
Earlier versions of these images will block the NU from Wave Cloud access.
The corresponding Coverage Units software images are:
  CU software: 700N036-xxx-057 (where xxx is a region-dependent 3-digit number)
  CU PIC: 700N040-002-070

## Slide 4: QUATRA 1000 behavior depending on NU/CU versions
NU | NU PIC | CU | CU PIC | Notes
700N036-033-055 and earlier | 700N046-003-047 and earlier | 700N036-033-055 and earlier | 700N040-002-070 | System cannot communicate with the cloud. Update NUs and CUs with the Wave Field Tool
700N036-033-055 and earlier | 700N046-003-047 and earlier | 700N036-033-056 | 700N040-002-070 | System cannot communicate with the cloud. Update NUs with the Wave Field Tool. Connect the system to the cloud, and CUs will update
700N036-033-056 | 700N046-003-048 | 700N036-033-056 | 700N040-002-070 | CU will update to 57, NU will update to 57
700N036-033-057 | 700N046-003-048 | 700N036-033-056 | 700N040-002-070 | CU will update to 57
700N036-033-056 / 700N036-033-057 | 700N046-003-048 | 700N036-033-055 and earlier | 700N040-002-070 | CU will not update (‘stranded’ CU). In this case the system will function, but the cloud will continually attempt to update the CUs and fail. The repeated updates will sometimes cause management actions to fail. Options: Manually update the CUs with the Wave Field Tool Wait for Nextivity software update in 2024, to cure the CU update failure.

## Slide 5: QUATRA 1000/2000 update with Wave Field Tool (WFT)
You need a PC with 2 networking connections (typically a laptop PC with Ethernet LAN and Wi-Fi interfaces)
The WiFi must provide an Internet connection
The LAN port must be set for DHCP (automatic IP address allocation)
The user logged into the PC must have administrative privileges, on that PC (have the ability to install software and change system settings)

## Slide 6: Minimum WFT version – 1.6.6.8
Wave Field Tool 1.6.6.8 must be used for the update
Earlier versions must be un-installed first
This is older than 1.6.6.8, therefore it must be un-installed

## Slide 7: Un-install any previous WFT versions

## Slide 8: Download the latest version
Download link: https://nextivityinc.com/software/wavefieldtool/

## Slide 9: Extract setup.exe & PCFieldTool.msi from WAVEFieldTool.zip
Then double-click setup.exe to install WFT 1.6.6.8

## Slide 10: Confirm the installation questions, during the install

## Slide 11
Network Unit

## Slide 12: While running WFT, you may have to disable Windows Firewall
When using WFT over Ethernet to Q1000 NU, it will most likely assume it is a Public network interface, so that will probably be the one you have to disable the firewall on

## Slide 13: Disable Windows Firewall (remember to turn back on after)

## Slide 14: Ethernet interface IP address
If your Ethernet interface is configured for automatic IP address allocation, when you plug it into the Q1000 NU Ethernet port, it will get an Autoconfiguration IPv4 address (169.254.x.x)

## Slide 15: Run WFT – ensure it is at least version 1.6.6.8

## Slide 16: Select Software Update
Press Scan for Ethernet Device

## Slide 17
WFT sets a static IP address on the Ethernet interface: 192.168.10.100
You will be asked for confirmation as an admin, to change the system settings.

## Slide 18: Scan for Ethernet Device

## Slide 19: Only Main Image, PIC Image and FPGA Hardware Image should be offered for update
If you are offered additional images, then you are probably running the wrong version of WFT
You should re-install the correct version

## Slide 20: FPGA Hardware Image is not usually required
When you select Update Software, the dialog box has a check-box for Update FPGA.
FPGA update is not usually required, even if it is showing an out-of-date version.
If you choose to do FPGA update, it takes about 10 minutes, compared to about 3 minutes without the FPGA update

## Slide 21: Update progress…

## Slide 22: Update progress…

## Slide 23: Update progress…

## Slide 24: Update progress…

## Slide 25: Update Complete
Note: if FPGA update was not selected, you may get a “Validation failed” message. In that case, the unit should still work (unless it previously had a corrupted FPGA image)

## Slide 26: Note on FPGA Hardware Image Update
Some devices may have a corrupted NU FPGA hardware image
In this case you should select the FPGA Update option when prompted
The update in this case will take approximately 10 minutes

## Slide 27: Confirmation dialog
When you select Update Software, the dialog box has a check-box for Update FPGA.

## Slide 28: Update progress…

## Slide 29: Update progress…

## Slide 30: Update progress…

## Slide 31: Update progress…

## Slide 32: Update Complete

## Slide 33: Set Ethernet Interface back to automatic IP address
After updating all the NUs you plan to update, you must manually reset the IPv4 settings on the Ethernet interface

## Slide 34: Set Ethernet Interface back to automatic IP address

## Slide 35
Coverage Unit

## Slide 36: CU Update - options
CU update is not mandatory
However, if you do not update the CU software, then if it has software older than version 56, it will not be updatable via the cloud
  That may be corrected in a future NU software update
CU software update is relatively slow (typically ~5 minutes)
If you decide to do CU software updates:
Connect your PC directly to the CU via micro-USB
Power the CU via Ethernet, from an NU
Re-start WFT, if you used it previously on NUs

## Slide 37: CU connections for WFT

## Slide 38: Run WFT: once synchronized, press Update Software

## Slide 39: Update progress…

## Slide 40: Update progress…

## Slide 41: Update progress…

## Slide 42: Update Complete (Bluetooth image update not essential)

## Slide 43
Thank you